## Slide 1
50 Ω stranded micro-coax · cryostat wiring
Insertion Loss & Heat-Load Projections
Two 50 Ω candidates for a 208-line harness — Samtec TCF-3450F and NEW N12-42M-100006-1 — projected across five assembly lengths: 3″, 5″, 10″, 15″, 18″.
Samtec TCF-3450F
34 AWG (7×42) SPC / FEP-foam / 46 AWG SPC serve shield, 50 Ω
Z₀
50.5 Ω
Cable OD
0.56 mm · 22.1 mils
α @ 2 GHz
0.637 dB/m
NEW N12-42M-100006-1
34 AWG (7×42) C27000 brass / PFA / 44 AWG brass spiral shield, 50 Ω
Z₀
49.8 Ω
Cable OD
0.71 mm · 28.0 mils
α @ 2 GHz
4.39 dB/m
Method — conductor loss after Pozar (Microwave Engineering, §2.7) plus dielectric loss, with a per-conductor stranding factor K_s calibrated to the TCF-3450F insertion-loss curve over 1–4 GHz. Heat load is steady-state conduction across each cryostat stage's ΔT, with lay-angle path corrections. Insertion loss is quoted at the 40 K → 4 K stage (T̄ ≈ 22 K); cross-sections are drawn to each preset's real geometry at a common scale.

## Slide 2
CABLE LENGTH
3″ assembly · 76 mm
PER-CABLE FIGURES · 50 Ω · 40 K → 4 K STAGE
Samtec TCF-3450F
34 AWG (7×42) SPC / FEP-foam / 46 AWG SPC serve shield, 50 Ω
Z₀ 50.5 Ω
OD 0.56 mm · 22.1 mils
RF INSERTION LOSS
2 GHz
0.049 dB
4 GHz
0.069 dB
CONDUCTED HEAT LOAD · PER CABLE
40 K → 4 K
35.3 mW
4 K → 1 K
566 µW
NEW N12-42M-100006-1
34 AWG (7×42) C27000 brass / PFA / 44 AWG brass spiral shield, 50 Ω
Z₀ 49.8 Ω
OD 0.71 mm · 28.0 mils
RF INSERTION LOSS
2 GHz
0.335 dB
4 GHz
0.475 dB
CONDUCTED HEAT LOAD · PER CABLE
40 K → 4 K
533 µW
4 K → 1 K
5.1 µW
Trade-off · TCF-3450F 6.9× lower loss · N12-42M 66× lower heat
Both cables are 50 Ω. Model — Pozar conductor loss + dielectric loss with a per-conductor stranding factor K_s calibrated to the TCF-3450F insertion-loss curve (1–4 GHz); heat load is steady-state conduction across each stage's ΔT with lay-angle path corrections. Insertion loss is quoted at the 40 K → 4 K stage. The two ratios are length-independent — they are the same on every length slide.

## Slide 3
CABLE LENGTH
5″ assembly · 127 mm
PER-CABLE FIGURES · 50 Ω · 40 K → 4 K STAGE
Samtec TCF-3450F
34 AWG (7×42) SPC / FEP-foam / 46 AWG SPC serve shield, 50 Ω
Z₀ 50.5 Ω
OD 0.56 mm · 22.1 mils
RF INSERTION LOSS
2 GHz
0.081 dB
4 GHz
0.115 dB
CONDUCTED HEAT LOAD · PER CABLE
40 K → 4 K
21.2 mW
4 K → 1 K
339 µW
NEW N12-42M-100006-1
34 AWG (7×42) C27000 brass / PFA / 44 AWG brass spiral shield, 50 Ω
Z₀ 49.8 Ω
OD 0.71 mm · 28.0 mils
RF INSERTION LOSS
2 GHz
0.558 dB
4 GHz
0.791 dB
CONDUCTED HEAT LOAD · PER CABLE
40 K → 4 K
320 µW
4 K → 1 K
3.1 µW
Trade-off · TCF-3450F 6.9× lower loss · N12-42M 66× lower heat
Both cables are 50 Ω. Model — Pozar conductor loss + dielectric loss with a per-conductor stranding factor K_s calibrated to the TCF-3450F insertion-loss curve (1–4 GHz); heat load is steady-state conduction across each stage's ΔT with lay-angle path corrections. Insertion loss is quoted at the 40 K → 4 K stage. The two ratios are length-independent — they are the same on every length slide.

## Slide 4
CABLE LENGTH
10″ assembly · 254 mm
PER-CABLE FIGURES · 50 Ω · 40 K → 4 K STAGE
Samtec TCF-3450F
34 AWG (7×42) SPC / FEP-foam / 46 AWG SPC serve shield, 50 Ω
Z₀ 50.5 Ω
OD 0.56 mm · 22.1 mils
RF INSERTION LOSS
2 GHz
0.162 dB
4 GHz
0.230 dB
CONDUCTED HEAT LOAD · PER CABLE
40 K → 4 K
10.6 mW
4 K → 1 K
170 µW
NEW N12-42M-100006-1
34 AWG (7×42) C27000 brass / PFA / 44 AWG brass spiral shield, 50 Ω
Z₀ 49.8 Ω
OD 0.71 mm · 28.0 mils
RF INSERTION LOSS
2 GHz
1.12 dB
4 GHz
1.58 dB
CONDUCTED HEAT LOAD · PER CABLE
40 K → 4 K
160 µW
4 K → 1 K
1.5 µW
Trade-off · TCF-3450F 6.9× lower loss · N12-42M 66× lower heat
Both cables are 50 Ω. Model — Pozar conductor loss + dielectric loss with a per-conductor stranding factor K_s calibrated to the TCF-3450F insertion-loss curve (1–4 GHz); heat load is steady-state conduction across each stage's ΔT with lay-angle path corrections. Insertion loss is quoted at the 40 K → 4 K stage. The two ratios are length-independent — they are the same on every length slide.

## Slide 5
CABLE LENGTH
15″ assembly · 381 mm
PER-CABLE FIGURES · 50 Ω · 40 K → 4 K STAGE
Samtec TCF-3450F
34 AWG (7×42) SPC / FEP-foam / 46 AWG SPC serve shield, 50 Ω
Z₀ 50.5 Ω
OD 0.56 mm · 22.1 mils
RF INSERTION LOSS
2 GHz
0.243 dB
4 GHz
0.346 dB
CONDUCTED HEAT LOAD · PER CABLE
40 K → 4 K
7.07 mW
4 K → 1 K
113 µW
NEW N12-42M-100006-1
34 AWG (7×42) C27000 brass / PFA / 44 AWG brass spiral shield, 50 Ω
Z₀ 49.8 Ω
OD 0.71 mm · 28.0 mils
RF INSERTION LOSS
2 GHz
1.67 dB
4 GHz
2.37 dB
CONDUCTED HEAT LOAD · PER CABLE
40 K → 4 K
107 µW
4 K → 1 K
1.0 µW
Trade-off · TCF-3450F 6.9× lower loss · N12-42M 66× lower heat
Both cables are 50 Ω. Model — Pozar conductor loss + dielectric loss with a per-conductor stranding factor K_s calibrated to the TCF-3450F insertion-loss curve (1–4 GHz); heat load is steady-state conduction across each stage's ΔT with lay-angle path corrections. Insertion loss is quoted at the 40 K → 4 K stage. The two ratios are length-independent — they are the same on every length slide.

## Slide 6
CABLE LENGTH
18″ assembly · 457 mm
PER-CABLE FIGURES · 50 Ω · 40 K → 4 K STAGE
Samtec TCF-3450F
34 AWG (7×42) SPC / FEP-foam / 46 AWG SPC serve shield, 50 Ω
Z₀ 50.5 Ω
OD 0.56 mm · 22.1 mils
RF INSERTION LOSS
2 GHz
0.291 dB
4 GHz
0.415 dB
CONDUCTED HEAT LOAD · PER CABLE
40 K → 4 K
5.89 mW
4 K → 1 K
94 µW
NEW N12-42M-100006-1
34 AWG (7×42) C27000 brass / PFA / 44 AWG brass spiral shield, 50 Ω
Z₀ 49.8 Ω
OD 0.71 mm · 28.0 mils
RF INSERTION LOSS
2 GHz
2.01 dB
4 GHz
2.85 dB
CONDUCTED HEAT LOAD · PER CABLE
40 K → 4 K
89 µW
4 K → 1 K
0.8 µW
Trade-off · TCF-3450F 6.9× lower loss · N12-42M 66× lower heat
Both cables are 50 Ω. Model — Pozar conductor loss + dielectric loss with a per-conductor stranding factor K_s calibrated to the TCF-3450F insertion-loss curve (1–4 GHz); heat load is steady-state conduction across each stage's ΔT with lay-angle path corrections. Insertion loss is quoted at the 40 K → 4 K stage. The two ratios are length-independent — they are the same on every length slide.

## Slide 7
SUMMARY
All five lengths at a glance
FULL HARNESS · 208 (13 cables of 16 lines)
Length | Samtec TCF-3450F |  |  |  |  | NEW N12-42M-100006-1 |  |  |  | 
 | LOSS | Q̇ PER CABLE |  | 208 (13 CABLES OF 16 LINES) |  | LOSS | Q̇ PER CABLE |  | 208 (13 CABLES OF 16 LINES) | 
 | 2 GHz | 40→4 K | 4→1 K | 40→4 K | 4→1 K | 2 GHz | 40→4 K | 4→1 K | 40→4 K | 4→1 K
3″ | 0.049 dB | 35.3 mW | 566 µW | 7.35 W | 117.6 mW | 0.335 dB | 533 µW | 5.1 µW | 110.9 mW | 1.06 mW
5″ | 0.081 dB | 21.2 mW | 339 µW | 4.41 W | 70.6 mW | 0.558 dB | 320 µW | 3.1 µW | 66.6 mW | 636 µW
10″ | 0.162 dB | 10.6 mW | 170 µW | 2.20 W | 35.3 mW | 1.12 dB | 160 µW | 1.5 µW | 33.3 mW | 318 µW
15″ | 0.243 dB | 7.07 mW | 113 µW | 1.47 W | 23.5 mW | 1.67 dB | 107 µW | 1.0 µW | 22.2 mW | 212 µW
18″ | 0.291 dB | 5.89 mW | 94 µW | 1.22 W | 19.6 mW | 2.01 dB | 89 µW | 0.8 µW | 18.5 mW | 177 µW
Insertion loss quoted at 2 GHz, 4–40 K stage — see the per-length slides for the 4 GHz figures. Heat load is the conducted Q̇ across each stage's ΔT, shown per cable and for the full harness (208 (13 cables of 16 lines)). The bundle columns are the per-cable figure × 208; they are the ones that set the cryostat budget.